## Slide 1: PDSe project: Analysis of Transport Protocols (TCP/QUIC) in Extreme Network Environments
Matěj Grégr, mgregr@fit.vut.cz

## Slide 2: PDSe project
Goal: Conduct a comparative analysis of different congestion control algorithms (TCP Reno, Cubic, BBR) within simulated "hostile" network environments
The project can be conducted through the following steps:
  Study different transport protocols and congestion algorithms in detail
  Set up a simple topology with at least two endpoints and one intermediate router (using VMs, Docker containers, or network namespaces).
  On the router, use tc (Traffic Control) to define three "extreme" network paths
    "Coffee Shop Wi-Fi": High random packet loss (3–5%) with low latency.
    "Starlink-style Satellite": High RTT (600ms+) and significant jitter.
    "The Bufferbloat Trap": Limited bandwidth with massive router queues (Deep Buffers), leading to extreme latency spikes under full load.
  Measure and benchmark at least two congestion algorithms
    Use iperf + wireshark to capture pcap and analyze protocol internals, e.g.how fast does the protocol recover to maximum speed after a packet loss event
  Create report (see below for recommendation)
  Present resuts and findings on project presentation

## Slide 3: Project report
The report structure should be as follows:
Introduction and description of transport protocols and congestion algorithms
Description of your network topology, monitoring set-up and used software
A set of scripts (Bash/Python) that automatically configure network parameters, run the measurements, and save the logs
CWND Visualization: Time-series plots showing how the Congestion Window changed over time for each protocol
Detailed methodology description.
In-depth explanation of why a protocol failed in a specific scenario (e.g., why Cubic underperforms on satellite links).
Proposed optimizations

## Slide 4: PDSe project
Project deadline: 21.4.2026 (hard deadline).
Presentations: 28.4.2026 during standard class
Maximum points: 20
Online consultations available using Moodle
Individual project – each student creates its own solution
Plagiarism prohibited – see copyrights and the publication policy